RC Light Controller

Addendum for Addressable LEDs
WS2811, WS2812

# Introduction
This document describes the function of an experimental firmware for the LANE Boys RC Mk4/Mk4P light controller that can drive Addressable LEDs.

This firmware addresses two use-cases:
- Ability to use LEDs connected to WS2811 ICs at each vehicle light (as used in Traxxas TRX4M)
- Animated full-color light bars such as “decel light” in drift cars
# Limitations
- Due to increased firmware size, only recent light controllers that are using the LPC824 micro-controller can be used
- WS281x devices are usually designed to operate from a stable 5V supply
- Some WS281x devices require the data line to carry a 5V signal, but the light controller only outputs a 3.3V signal so a level-shifter may be required
- There is no polarity protection in WS281x devices, connecting them wrong by accident instantly destroys the WS281x devices
- WS281x devices adjust brightness using pulse width modulation, which can cause flickering in videos
- The firmware supports strings of up to 20 WS281x devices
- The firmware only supports one specific WS281x timing protocol

All these limitation mean that WS281x devices are only suitable for people some degree of knowledge in electronics.
# Connecting WS281x devices
WS281x devices have have three inputs: Supply (+) and (-), and a DI (data input) line.
On the light controller side the WS281x data can be output on OUT/ISP, TH/Tx and OUT15S pin.
OUT/ISP is conveniently accessible on the right side of the Mk4P light controllers, so it is a good choice.
Connecting WS281x devices to TH/Tx is only possible if the Light Controller is using Pre-Processor input, i-Bus or S.Bus – but not when Servo inputs are used.
The WS281x data signal can also output on the switched light output OUT15S. A pull-up resistor of about 470 Ohm is required.
The switching transistor on OUT15S inverts the data signal. To compensate for the inversion the Configurator provides an option to send an inverted signal.
Using OUT15S with a pull-up connected to 5V acts as a “level shifter”, generating a 5V data signal as required by some WS281x devices. In contrast, OUT/ISP and TH/Tx output a 3.3V data signal, which is not compatible with some WS281x devices.
# Configuration
The experimental firmware can be accessed through a special version of the Configurator at https://laneboysrc.github.io/rc-light-controller/configurator-ws281x.html
This firmware is restricted in function, for example it does not support Slave mode. For those standard functions please use the normal Configurator at https://laneboysrc.github.io/rc-light-controller
Start by defining the Operating mode.
Then enable the WS281x output in the Output functions tab.
[insert image]
Assign the WS281x to the desired pin on the Light Controller. When using OUT15S or an external inverting buffer on the other pins, check the Invert WS281x output signal level checkbox.
# Single color LEDs connected to WS2811
The WS2811 device is a generic LED driver IC. It has three LED outputs. One could place one WS2811 IC at each “corner” of the car and drive the corresponding LEDs. For example, the right front headlight would have a parking light LED, one for high beam, and an orange one for indicator, all connected to a single WS2811. Similar on the left front. On the rear right another WS2811 would drive a red LED for combined tail/brakelight function, an orange LED as indicator, and a white LED as reversing light. Same for rear left.
The four WS2811 devices are daisy-chained and the the first WS2811 in the chain gets connected to the light controller.
Such a configuration is applied in the Traxxas TRX4M light kit.
The LEDs connected to the WS2811 IC can be controlled as Slave in the light controller configuration. When WS281x output is enabled the first 15 Slave LEDs are mapped to the WS2811 chain. This implies that up to 5 WS2811 ICs can be used, each driving 3 LEDs for a total of 15 LEDs.
# Animations and RGB LEDs
For more advanced LED configurations such as color LEDs and animations, it is possible to control the WS281x through light programs. Light programs are small scripts executed by the light controller. Light programs are available for Mk4, Mk4P and Mk4S since the inception, but now have been extended in this experimental firmware with functions for Addressable LEDs.
Light programs require a certain amount of programming skills, which not everyone has. If you need assistance feel free to reach out to laneboysrc@gmail.com
For a full documentation of the light programs including addressable LED functions please refer to the separate manual at https://github.com/laneboysrc/rc-light-controller/blob/ws281x/mk4-tlc5940-lpc812/doc/light-programs-ws821x.md

# Timing? Data voltage?
# Verify if your light controller is suitable to run the Addressable LED firmware
# Source code