RC Light Controller

Addendum for Addressable LEDs
WS2811, WS2812

# Introduction
This document describes an experimental firmware for the LANE Boys RC Mk4/Mk4P light controller that can drive Addressable LEDs.

This firmware addresses two use-cases:
- Ability to use LEDs connected to WS2811 ICs at each vehicle light (as used in Traxxas TRX-4M)
- Animated full-color light bars such as “decel light” in drift cars
# Limitations
- Due to increased firmware size, only recent light controllers that are using the LPC824 micro-controller can be used
- WS281x devices usually require a stable 5V supply
- Some WS281x devices require a 5V logic signal on the data line, but the light controller only outputs a 3.3V signal. A level-shifter may be required
- There is no polarity protection in WS281x devices; reversing power by accident instantly destroys the WS281x devices
- WS281x devices adjust brightness using pulse width modulation, which can cause flickering in videos
- The firmware supports strings of up to 20 WS281x devices
- The firmware only supports one specific WS281x timing protocol

All these limitation mean that WS281x devices are only suitable for for some use cases and users with a moderate amount of knowledge in electronics.
# Connecting WS281x devices
WS281x devices have three inputs: Supply (+) and (-), and a DI (data input).
On the light controller side the WS281x data can be output on OUT/ISP, TH/Tx and OUT15S pin.
OUT/ISP is conveniently accessible on the right side of the Mk4P light controllers, so it is a good choice.
Connecting WS281x devices to TH/Tx is only possible if the Light Controller is using Pre-Processor input, i-Bus or S.Bus – but not when Servo inputs are used.
The WS281x data signal can also output on the switched light output OUT15S. A pull-up resistor of about 470 Ohm is required. The switching transistor on OUT15S inverts the data signal. To compensate for the inversion the Configurator provides an option to transmit an inverted signal to compensate for the transistor.
Using OUT15S with a pull-up connected to 5V acts as a “level shifter”, generating a 5V data signal as required by some WS281x devices. In contrast, OUT/ISP and TH/Tx output a 3.3V data signal, which is not compatible with some WS281x devices.
# Configuration
The experimental firmware can be accessed through a special version of the Configurator at https://laneboysrc.github.io/rc-light-controller/configurator-ws281x.html
This firmware is restricted in function, for example it does not support Slave mode or programming Pre-Processors. For those standard functions please use the normal Configurator at https://laneboysrc.github.io/rc-light-controller
Start by defining the Operating mode.
Then enable the WS281x output in the Output functions tab.
[insert image]
Assign the WS281x to the desired pin on the Light Controller. When using OUT15S or an external inverting buffer on the other pins, check the Invert WS281x output signal level checkbox.
# Single color LEDs connected to WS2811
The WS2811 device is a generic LED driver IC. It has three LED outputs. One could place one IC at each “corner” of the car and drive the corresponding LEDs.
For example, the right front light cluster would have a parking light LED, one for high beam, and an orange LED as indicator, all connected to a single WS2811. Similar on the left front.
On the left right another WS2811 would drive a red LED for combined tail/brake light function, an orange LED as indicator, and a white LED as reversing light. Repeat for rear right.
The four WS2811 devices are daisy-chained and the the first WS2811 in the chain gets connected to the light controller.
Image
Such a configuration is applied in the Traxxas TRX-4M light kit.
The LEDs connected to the WS2811 IC can be controlled as Slave in the light controller configuration. When WS281x output is enabled, the first 15 Slave LEDs are mapped to the WS2811 chain. This implies that up to 5 WS2811 ICs can be used, each driving 3 LEDs for a total of 15 LEDs.
# Animations and RGB LEDs
For more advanced LED configurations such as color LEDs and animations, it is possible to control the WS281x through light programs. Light programs are small scripts executed by the light controller. Light programs are available for Mk4, Mk4P and Mk4S since the inception, but now have been extended in this experimental firmware with functions for Addressable LEDs.
For a full documentation of the light programs including addressable LED functions please refer to the separate manual at https://github.com/laneboysrc/rc-light-controller/blob/ws281x/mk4-tlc5940-lpc812/doc/light-programs-ws821x.md
Light programs require a certain amount of programming skills. If you need assistance feel free to reach out to laneboysrc@gmail.com
# WS281x device compatibility
To check whether a particular WS281x device is compatible with this experimental light controller firmware, we need to consult the data sheet of the WS281x intended to be used.
If there is no data sheet for your device, for example when purchasing random WS2812 LEDs from on-line shops, then there is no way to determine up-front whether the devices will work with this experimental firmware.
## Supply voltage
Almost all WS281x devices are designed to operate at 5V and tolerate at most 5.5V. Unless your RC system (BEC, receiver) runs on 5V, a separate 5V voltage regulator is required.
## Signal voltage of the DI line
The Data Input (DI) line of the WS281x requires certain voltages to determine whether a logic 0 or logic 1 is being transmitted.
For many WS281x devices the specification for a logic 1 signal on the DI line is a minimum voltage of 0.7 × Vdd. Vdd is the supply voltage of the WS281x device. At 5V, the DI line must have a voltage of no less than 0.7 × 5V = 3.5V to be recognized as logic 1.
The micro-controller in light controller operates at 3.3V. This means that it can output at most 3.3V, which is below the minimum that many WS281x accepts as logic 1.
For such devices a level-shifter is required, which converts the 3.3V logic to 5V logic. Note that the level-shifter must support data rates of at least 5 MHz.
Some WS281x devices are designed to work with 3.3V logic. For example the Worldsemi WS2812C-2020-V1 RGB LED requires only 2.7V for logic 1.
## Timing protocol
The basic WS281x protocol is always the same, but the timing values differ between various specific devices.

Timing diagram as shown in the WS8211 datasheet
There are 5 timing values relevant for the protocol.
T0H: the time the DI line is high when transmitting a logic 0 data bit
T0L: the time the DI line is low when transmitting a logic 0 data bit
T1H: the time the DI line is high when transmitting a logic 1 data bit
T1L: the time the DI line is low when transmitting a logic 1 data bit
Reset: the time that indicates to the WS281x device that a packet has been completed

The light controller outputs the following timing values:
T0H: 250ns
T0L: 750ns
T1H: 750ns
T1L: 250ns
Reset: >1ms

These values are suitable for the WS2811 device, for which the datasheet requires:
T0H: 220-380ns
T0L: 580-1000ns
T1H: 580-1000ns
T1L: 220-420ns

The WS2812C-2020-V1 datasheet states different requirements:
T0H: 220-380ns
T0L: 580-1000ns
T1H: 580-1000ns
T1L: 580-1000ns
However, testing showed that the WS2812C-2020-V1 still works fine with the experimental firmware, despite T1L being outside of the specification.
# Verify if your light controller is suitable to run the Addressable LED firmware
Due to the increased size of the firmware, only light controllers built from 2022 onward using the NXP LPC824 micro-controller can be used.
You can check with your light controller has the correct micro-controller using the following steps:
- Load https://laneboysrc.github.io/rc-light-controller/programmer.html
- Connect the light controller to your WebUSB programmer
- Press the Read button
- In the diagonstics window look for the following information
Add screenshot
Of it says anything else than LPC824 (e.g. LPC812 or LPC832) then your light controller is not compatible with this experimental firmware.
# Source code
The experimental software for Addressable LEDs is kept in a separate branch named ws281x in the Github repository of the light controller.
It can be accessed through the following link:
https://github.com/laneboysrc/rc-light-controller/tree/ws281x